## Slide 1: Intro to Lockpicking

## Slide 2: First, a word about rules…
Yes, we have rules. 
  Do not pick locks which you do not own.
  Do not pick locks upon which you rely.
Notes: VENUE locks!
Legal reasons, but also moral reasons. We teach ethical lockpicking.

## Slide 3: The Three Kinds of Lock-Opening

## Slide 4: The Three Kinds of Lock-Opening
  Lockpicking – what we do TOOOL provides the knowledge and the means – what spies do TOOOL provides neither knowledge nor means

## Slide 5: The Three Kinds of Lock-Opening
  Lockpicking TOOOL provides the knowledge and the means
  Quick & Dirty TOOOL provides neither knowledge nor means
Notes: Engage with the lock. Love the lock.
Bump keys

## Slide 6: The Three Kinds of Lock-Opening
  LockpickingTOOOL provides the knowledge and the means
  Quick & Dirty TOOOL provides knowledge. . . but no means
  Covert & High-Tech TOOOL provides neither knowledge nor means

## Slide 7: The Three Kinds of Lock-Opening
  Lockpicking – what we do TOOOL provides the knowledge and the means
  Quick & Dirty – what criminals do TOOOL provides knowledge. . . but no means
  Covert & High-Tech – what spies do TOOOL provides neither knowledge nor means

## Slide 8: The Three Kinds of Lock-Opening
  Lockpicking – what we do TOOOL provides the knowledge and the means
  Quick & Dirty – what criminals do TOOOL provides knowledge. . . but no means
  Covert & High-Tech – what spies do TOOOL provides neither knowledge nor means

## Slide 9: Lockpicking is Simple!
Notes: Two tools. Not one. Not three. Not a screwdriver and a pen knife. Two tools. More on this later.

## Slide 10: Pin Tumbler Locks

## Slide 11: Pin Tumbler Locks

## Slide 12: Pin Tumbler Locks

## Slide 13: Outer View

## Slide 14: Outer View
Body
Keyway
Key pin
Plug

## Slide 15: Inner View

## Slide 16: Anatomy of a Lock
Spring
Driver pin
Key pin
Plug

## Slide 17: Anatomy of a Lock
Spring
Driver pin
Key pin
Plug
Shear line
Notes: We call the key pin and the driver pin together a “pin stack” because it’s, well, a stack. Of pins.

## Slide 18: Attempt Without a Key
Notes: Plug moves a bit, but not much. How far? Only until it gets stopped by the driver pin. That’s the driver pin’s job: Stop the plug from turning unless the driver pin has been pushed to the right height. What usually pushes the pin stack up so the driver pin is at the right height? Yeah, the key.

## Slide 19: Operating With a Key

## Slide 20: Pin Stacks
Notes: This is a lock at rest, without a key in it, and with the driver pins stuck halfway between the plug and the housing, blocking the plug from turning.
As you can see, all of the driver pins are the same size (height), but all of the key pins are different heights.
This is what makes each lock take a different key, because only a key cut to make up for the varying heights of the key pins can even out the differences and create a clear uninterrupted shear line.
(Note: The pins don’t fall all the way down to the bottom of the lock because the drilled hole that each pin is in tapers to the bottom so that the key can get in but the pin can’t get out. Go back and look at the previous slide to see how this works.)

## Slide 21: Key Operation

## Slide 22: One Bitting Too Low
Notes: Unlike horseshoes and hand grenades, close doesn’t count here. Only when every pin stack is moved to the right height

## Slide 23: One Bitting Too High
Notes: Replaced one problem with another.

## Slide 24: In a Perfect World
Notes: If the lock were perfectly manufactured, lockpicking would not be possible.

## Slide 25: In the Real World
Notes: In the real world, locks cost money and so they have to be made cost effectively. Often, this means “cheaply”. Equipment gets old, it gets misaligned, it gets dull, it rattles. The lower cost the lock, the lower the specification, the more room for mechanical defects.

## Slide 26: In the Real World
Notes: Miscast, pitted, rough, rusted, all of the parts of a lock can have small defects that make them work not quite right.

## Slide 27: In the Real World
Notes: The most important defect for us as lockpickers is the misalignment of the pin holes.
As the holes are drilled, they are fractions of a millimeter off center in a random deviation.
This is an exaggeration, but the it shows the principle. The dotted line provides a reference to highlight the misalignment of the pin holes.
All of the pin holes are going to be slightly off center one direction or another, but one of them will be MOST off center. This is where we start.
Here’s why:

## Slide 28: Attempt Without a Key
Notes: Let’s just consider the one pin that is most off center. (In the diagram on the last slight, it’s the 4th pin. [You can have the audience answer this to make sure they’re tracking])
As we’ve seen, if you try to turn a lock plug without a key, it doesn’t open, but something happens.
The plug has a little bit of play before it stops.
What is it stopping against? The first thing it runs into is the most out of line pin.
So it stands to reason that if we move that pin out of the way, it will be able to continue turning.

## Slide 29: “Setting” a Binding Pin
Notes: To move the driver pin out of the way, we use a pick to push up on the key pin (red pin).
Once the driver pin is high enough that it’s out of the way, the plug turns ever so slightly.
Now the hole that the driver pin went up through is no longer there.
The driver pin is trapped; it can’t go back the way it came.
This is setting a pin, and once you’ve set a pin you can basically forget about it as long as you keep a little bit of turning tension on the plug.

## Slide 30: The Key Pin Can Still Move Freely
Notes: The key pin is isolated from the spring.

## Slide 31: Setting Multiple Pins

## Slide 32: Take Caution to Avoid Over-Lifting
Notes: Don’t replace one problem with another.

## Slide 33: The Turning Tool

## Slide 34: Lockpicking is Simple! (redux)
Notes: We talked about what the pick does, now we talk about what the tension tool does.

## Slide 35: Turning Tool
Notes: Different sizes fit in different keyways; if the tool you’re using doesn’t sit well, try another one.

## Slide 36: Bad Turning Tool Usage (Pulling)

## Slide 37: Better Turning Tool Usage (Pushing)

## Slide 38: Best Turning Tool Usage (Pushing Out at Tip)

## Slide 39: Good Turning Tool Pressure

## Slide 40: Too Much Turning Tool Pressure!

## Slide 41: Which Pick do I use?

## Slide 42: Different Shapes for Different Purposes
Notes: DON’T BEND MY TOOLS!

## Slide 43: Hook: Direct Lifting

## Slide 44: Hook: Rocking Lifting

## Slide 45: Be gentle!
Notes: If you like to do the rocking lifting style, be careful not to use the pick as a crowbar.
If it’s not lifting with gentle pressure, something isn’t right (probably too much turning pressure or already overset) and cranking harder won’t help.
Don’t make the bunny cry.

## Slide 46: Half-Diamond: Raking/Shoveling
Notes: The hook/finger is great for hitting individual pins very specifically, but it pretty much forces you to release and reengage with each new pin.
The half diamond pick is a nice compromise because you can both individually pick but also move fairly smoothly from one to the other.
The advantage is you move more easily, the disadvantage is it may make it just a little bit more difficult to keep track of which pin you’re on.

## Slide 47: Half-Diamond: Counting Pins
Notes: Whenever you encounter a new lock, a great first step is to count the pins.
This will give you an idea of how difficult the lock is, as well as where the pins are and what they sound like.
You’ll need a tool with a flat back on it, which usually means a half diamond.
Shove it all the way to the back of the lock.

## Slide 48: Half-Diamond: Counting Pins
Notes: Then live the whole thing upward together like a tray, lifting all the pins and compressing all the springs.

## Slide 49: Half-Diamond: Counting Pins
Notes: Once all of the pins are lifted and all of the springs are loaded, be ready to listen and feel.
Maybe hold it up to your ear.

## Slide 50: Counting Pin Stacks
Notes: Carefully draw the pick out of the lock.

## Slide 51: Counting Pin Stacks
Notes: As you slide off each pin, the spring will expand, shooting the pins down to the bottom of the lock with a snap that you can hear and feel.

## Slide 52: Raking

## Slide 53: Raking

## Slide 54: “Raking” vs. “Lifting”

## Slide 55: Raking

## Slide 56: Raking

## Slide 57: Lifting

## Slide 58: What is Jiggling ?
In Between Raking & Lifting …

## Slide 59: What is Jiggling ?
… There is “Jiggling”

## Slide 60: What is in your kit? Picks
Hook
Reach
Offset Half-Diamond
Half-Diamond
Half-Diamond (hollow)
Rake

## Slide 61: What is in your kit? Turning Tools
Different widths
Different thicknesses
Different lengths

## Slide 62: What is in your kit? Turning Tools
Different widths
Different thicknesses
Different lengths
Why?

## Slide 63: What is in your kit? Turning Tools
Different widths
Different thicknesses
Different lengths
Why?
Different tools fit
different keyways
In different ways.

## Slide 64: Turning Tool Position: “Edge of the Plug”

## Slide 65: “Standard” Turning Tools

## Slide 66: Space in the Keyway

## Slide 67: Space in the Keyway

## Slide 68: Careful to not Cause Extra Friction

## Slide 69: “Standard” vs “Flat” Turning Tools

## Slide 70: Turning Tool Position: “Center of the Plug”

## Slide 71: More Space in the Keyway

## Slide 72: Turning Direction

## Slide 73: Turning Direction

## Slide 74: Who Wants To Try?

## Slide 75: Starter Exercises – Lift without tension

## Slide 76: Starter Exercises – Lift without tension

## Slide 77: Starter Exercises – Lift with tension

## Slide 78: Starter Exercises – Lift with tension

## Slide 79: Practice Locks

## Slide 80: FAQs
✔
✗

## Slide 81: The Two Most Important Things…
RELAX

## Slide 82: The Two Most Important Things…
OPEN!

## Slide 83
Washington, D.C.
Philadelphia, PA
New York, NY
Rochester, NY
Want more?

## Slide 84
  Questions?

## Slide 85: Pick-Resistant Locks

## Slide 86: Pick-Resistant Keyways
Simple… … straight and wide

## Slide 87: Pick-Resistant Keyways
Simple… … straight and wide
Medium… … straight but narrow

## Slide 88: Pick-Resistant Keyways
Simple… … straight and wide
Medium… … straight but narrow
Complex… … thinner and curvy

## Slide 89: Pick-Resistant Keyways
Simple… … straight and wide
Medium… … straight but narrow
Complex… … thinner and curvy
Hard… … lots of angles

## Slide 90: Pick-Resistant Keyways
Simple… … straight and wide
Medium… … straight but narrow
Complex… … thinner and curvy
Hard… … lots of angles
Fiendish… … overlapping wards

## Slide 91: Pick-Resistant Pins

## Slide 92: Pick-Resistant Pins – Spool Pin

## Slide 93: Pick-Resistant Pins – Spool Pin Binding

## Slide 94: Pick-Resistant Pins – Spool Pin Picking

## Slide 95: Pick-Resistant Pins – Mushroom Pin

## Slide 96: Pick-Resistant Pins – Serrated Pin

## Slide 97: Pick-Resistant Pins – ASSA “Sneaky” Pin

## Slide 98: Pick-Resistant Pins – TrioVing “Double Mushroom” Pin

## Slide 99: Pick-Resistant Locks
a substantial improvement…
…can be picked, but only with much skill and time

## Slide 100
  Questions?

## Slide 101: Resources for Learning More

## Slide 102: Resources For Learning More
Books
  Practical Lock Picking & other books by Deviant Ollam
  High Security Mechanical Locks by Graham Pulford
  Locks, Safes, & Security by Marc Tobias
Videos
  YouTube & Google
  http://connect.waag.org/toool
  http://deviating.net/lockpicking/videos.html
On The Web
  http://toool.us ‒ http://toool.nl
  http://blackbag.nl ‒ http://deviating.net

## Slide 103: Resources For Learning More

## Slide 104: Legal Questions
We are not lawyers
Purchase/Shipping through mail
  Lock manufacturer
  Auto dealer
  Law enforcement
  Repo man
  Bona fide locksmith
Possession & use
  Burglary tools statutes
  During an illegal act

## Slide 105: Legal Questions
Legal by statute
Legal, no criminal statute
Legal, but note other laws
Prima Facie clause
Picks are more restricted
http://toool.us/laws.html

## Slide 106: Acquiring Locks
Free
  Basements, garages, yard sales
  Ask neighbors, ask locksmiths
For sale
  Vary your sources
  Hardware store vs. eBay
Specialized
  Progressive kits
  Ultimate practice lock

## Slide 107
Washington, D.C.
Philadelphia, PA
New York, NY
Rochester, NY
Want more?